Lesson 10
Combinational Logic
Mohd Saufy Rohmad
Technical Trainer and Consultant

---
Simple Combinational Logic
- Any section of logic that doesnt have any memory elements is considered as a combinational logic.
- So the simplest combinational logic represents a wire, for example,
- wire1 <= wire2;
- It means wire2 is connected to wire1.
- As mentioned in the previous lesson, we can create logic gates in the following way (lesson 5),
- Q <= AB + BC(B+C);
- We can visualize this logic here. Note that, A, B, C and Q are all translated as ports/wires.

---
Simple Combinational Logic
- We can also write simple arithmetic units in this fashion (Hour 8),
- C <= resize(A+B,9);
- Here, A and B both have 8 wires to support 8-bit inputs. C has 9 wires for 9-bits.

---
Conditional Statements
- We will encounter scenarios where we need a conditional statements.
- How can we use conditional statements as combinational logic? We will see that in this section.
- As an example, we will create the most basic 2:1 multiplexers with several conditional statements.
- Lets assume our multiplexer is selecting between inputs A and B based on the value of "Selector". If Selector is 0, the output will be A and if Selector is 1, the output will be B.

---
When / Select
It is possible the design the multiplexer with when-select keyword. The code is given below,

---
When / Select
When-select is very useful for writing short codes. Another example of the when-select is,
C <= "1000" when selector = "00" else
"0100" when selector = "01" else
"0010" when selector = "10" else
"0001" when selector = "11";

---
With/Select/When
- It is possible the design the multiplexer with with-select keyword.
- It is very similar to When-Select. The code is given below,
  Library ieee;
  use ieee.std_logic_1164.all;
  use ieee.numeric_std.all;
  entity mux_with is
  port(
  A,B: in unsigned(7 downto 0);
  Selector: in std_logic;
  C: out unsigned(7 downto 0));
  end mux_with;
  architecture mux_with_arch of mux_with is
  begin
  with selector select
  C <= A when '0',
  B when others;
  end mux_with_arch;

---
With-select-when can also be very useful, for example,
with selector select C <=
"1000" when "00",
"0100" when "01",
"0010" when "10",
"0001" when "11";

---
Process (if else statement)
- We will introduce a very important construct for the VHDL language called process. Any if-else or case statement should be inside the process construct.
- Any process should have the following structure,
  process(sensitivity_list)
  begin
  VHDL_code (if-else and case statements goes here)
  end process;
  A 2:1 multiplexer can also be written with if-else inside a process as,

---
Process (case statement)

---
Thank You