Lesson 11
Combinational Logic (part 2)
Mohd Saufy Rohmad
Technical Trainer and Consultant

---
if-else vs case
- In the last hour we demonstrated how to design a 2:1 multiplexer with if-else and case.
- So one might think that logic constructed with if-else and case will be same always.
- But its not.
- Whenever we are going for more than 2 inputs in a multiplexer, then if-else and case creates different type of logic.
- Take a look at the following code,

---
if-else vs case
To create a 4:1 mux, we need to use the following VHDL with a case statement,

---
Latch Inference
- We have to be very careful while writing the if-else and case statements.
- If they are not written properly, a latch can be created at the output.
- This latches can mess up the whole timing result.
- Therefore, the circuit might give wrong results at the output.

---
Sensitivity List
- The sensitivity list includes all the signals that works as an input in a combinational process.
- The signals of the sensitivity list are included in the parentheses next to the process keyword in VHDL.
  process(sensitivity list)
- In the example given above, A,B,C,D and Selector are all input signals of the 4:1 multiplexer. Thats why all of them should be in the sensitivity list.
  process(A,B,C,D,Selector)
- Include all the input signals in the process sensitivity list for combinational logic
- Failure to include all the input signals would result in a unwanted behavior in the simulation. This is one of the most common mistakes of VHDL.

---
If-Else
This if-else is wrongly written,
process(state)
begin
if state = "001" then
cs <= "01";
elsif state = "010" then
cs <= "10";
elsif state = "100" then
cs <= "11";
end if;
end process;

---
If / else
Because, it did not specify each possible state. This will create output latches. The correctly written case statement would be,
process(state)
begin
if state = "001" then
cs <= "01";
elsif state = "010" then
cs <= "10";
elsif state = "100" then
cs <= "11";
else
cs <= "00";
end if;
end process;

---
Case
This case statement is wrongly written,
process(state)
begin
case(state) is
when "001" =>
cs(0) <= '1';
when "010" =>
cs(1) <= '1';
when "100" =>
cs(1 downto 0) <= "11";
when others =>
cs(1 downto 0) <= "00";
end case;
end process;

---
Case
- Because, it did not specify all possible outputs for each state.
- This will create output latches. The correctly written case statement would be:
  process(state)
  begin
  cs <= "00";
  case(state) is
  when "001" =>
  ...

---
Thank You