Lesson 12
Testbench
(Combinational Logic)
Mohd Saufy Rohmad
Technical Trainer and Consultant

---
Testbench
- A major part of digital design is testing with simulation.
- A designer should never be satisfied if a VHDL code doesnt show any compilation or synthesis error.
- The design needs to be simulated with different inputs to see whether we are getting the correct output.
- The question is, how to simulate a circuit written in VHDL?
- There comes the testbenches.
- A testbench is another entity that takes the design under test (DUT) as a component.
- In this lesson, we will talk about testbenches written for combinational logics.
- We wrote an 8-bit adder in lesson 5. The entity was written as:

---
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity adder_8bitc is
port (
A,B: in unsigned(7 downto 0);
C : out unsigned(8 downto 0) );
end adder_8bitc;
architecture adder_8bitc_arch of adder_8bitc is
begin
C <= resize(A+B,9);
end adder_8bitc_arch;

---
Testbench
- We want to test this circuit.
- So we need a testbench.
- We create an entity testbench_tb that doesnt have any input or output ports.
- This entity contains the adder_8bitc entity as a component.
- The input and output ports are connected to a few signals instantiated in the testbench_tb entity.
- We can feed these signals with different input values at different time instances and check the output.
- The code of the testbench is given below,

---
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity testbench_tb is
end testbench_tb;
architecture testbench_arch of testbench_tb is
component adder_8bitc is
port (
A,B: in unsigned(7 downto 0);
C : out unsigned(8 downto 0) );
end component;
signal A: unsigned(7 downto 0) := (others=>'0');
signal B: unsigned(7 downto 0) := (others=>'0');
signal C: unsigned(8 downto 0) := (others=>'0');

---
begin
adder_8bi: adder_8bitc port map(
A => A,
B => B,
C => C);
process
begin
wait for 100 ns;
A <= "00000010";
B <= "00000011";
wait for 10 ns;
A <= "00000110";
B <= "00000101";
wait;
end process;
end testbench_arch;

---
Testbench
- In this case, we fed the inputs of adder_8bi with some values after 100ns.
- Then we wait for 10ns and feed next input values again.
- Afterwards, we wait indefinitely.
- Recall lesson 10, where we stated how behavioral codes use some extra features of VHDL language that are not supported for synthesis.
- The wait statements are not synthesizable.
- However, we don’t also want to synthesize the testbench.
- We just want to use this part of the code for testing.

---
Run on ModelSim
After compiling the above code click on the "library" (circle 1)>click on "work" (circle 2)>click "testbench_tb" (circle 3) as the project name was that. Then you will find the architecture file. Right click on that and select "Simulate".

---
Thank You