Lesson 21
Variables
Mohd Saufy Rohmad
Technical Trainer and Consultant

---
Variables
- Variables can be very useful for using integers in VHDL coding.
- Applying integers in VHDL makes life easier for a digital designer.
- A very useful example of applying variables can be found in the counter designs shown in the Intel's site.
- The link is given below:

---
Variables
- There is a difference between signal and variable in a process.
- Signals in a variable are updated instantly at the time of the trigger, while variables in a process are computed sequentially one after another. An example will clarify things.
- Lets assume, we have, x1 = 1, x2 = 2 and x3 = 3.
- We want to compute,
- x1 = x2;
- x2 = x1 + x3;
- x3 = x2;
- We will first use x1, x2 and x3 as signals and then as variables inside a process.
- The first example of x1,x2 and x3 being signal is given below.

---
----------------------------------
----- Signal in a process ------
----------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.STD_LOGIC_ARITH.ALL;
entity SIG_test is
Port ( Trig : in STD_LOGIC;
Res : out STD_LOGIC_VECTOR (31 downto 0));
end SIG_test;
architecture SIG of SIG_test is
signal signal1: STD_LOGIC_VECTOR(31 downto 0) := "00000000000000000000000000000001";
signal signal2: STD_LOGIC_VECTOR(31 downto 0) := "00000000000000000000000000000010";
signal signal3: STD_LOGIC_VECTOR(31 downto 0) := "00000000000000000000000000000011";
begin
process(Trig)
begin
signal1 <= signal2;
signal2 <= conv_std_logic_vector(signed(signal1) + signed(signal3),signal2'length);
signal3 <= signal2;
Res <= conv_std_logic_vector(signed(signal1) + signed(signal2) + signed(signal3),Res'length);
end process;
end SIG;
example

---
----------------------------------
----- Variables in a process ------
----------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.STD_LOGIC_ARITH.ALL;
entity VAR_test is
Port ( Trig : in STD_LOGIC;
Res : out STD_LOGIC_VECTOR (31 downto 0));
end VAR_test;
architecture VAR of VAR_test is
begin
process(Trig)
variable variable1: integer :=1;
variable variable2: integer :=2;
variable variable3: integer :=3;
begin
variable1 := variable2;
variable2 := variable1 + variable3;
variable3 := variable2;
Res <= conv_std_logic_vector(variable1 + variable2 + variable3,Res'length);
end process;
end VAR;
2nd example

---
Elaboration
- In the first example,
- Res = 8, while using x1, x2 and x3 as signals
- So, in the first one when x1 <= 1, x2 <= 2, x3 <= 3,
- the computations inside the process works like,
- x1 <= x2; --- x1 becomes 2
- x2 <= x1 + x3; --- x2 becomes 1+3 = 4, note that, the result of x2 does not use the updated value of x1
- x3 <= x2; ---- x3 becomes 2, note that, the result of x3 does not use the updated value of x2
- So, when triggered, all the computations use the present values of x.
- In the second example,
- Res = 12, because x1, x2 and x3 are updated in each line, in other words, work sequentially.

---
Thank You