Lesson 5
Entity, Architecture and Signals
Mohd Saufy Rohmad
Technical Trainer and Consultant

---
Think In Hardware
- Think about an IC, for example, a 7400N IC.
- It includes four NAND gates inside, while its provided in a black package.
- Lets say we want to write the VHDL code of the 7400N IC

---
Think In Hardware
- It is easier to think that you are designing a black box when you are writing any VHDL code.
- This black box has inputs and outputs and something in between.
- This black boxes are called entity.

---
Think In Hardware
- For 7400N IC's VHDL code, we will call this black box aka entity as IC7400. The entity IC7400 should have 8 input ports and 4 output ports corresponding to the input and outputs of the original 7400N IC.
- This is how the VHDL code of IC7400 might look like

---
Think In Hardware

---
Architecture
- Every entity can have different architecture.
- Think about it in this way that any digital circuit can have different architectures, i.e. different logic, different number of gates etc.
- For example, The output of the following circuit have a boolean expression of AB + BC(B+C) which can be simplified as B(A+C).
- The VHDL code of the unoptimized architecture, i.e. AB + BC(B+C) can be written as

---
VHDL for 7400N
The VHDL code of the unoptimized architecture, i.e. AB + BC(B+C) can be written as,

---
VHDL for 7400N
And the optimized architecture can be written as,

---
Signal
- So far we have only seen how to write input and output ports.
- We only learned to think the entity as a blackbox where the input and output ports are coming out of the box.
- But what happens when we have to write some ports or wires inside the blackbox.
- For example, consider the following circuit.
- The final output is (A or B) and C.
- It is possible to write the whole thing in a single sentence.
- But we might have a complex design where its not possible.
- We have to breakdown the entire operation then.
- In this case, lets say, we want to break down (A or B) and C into (A or B) first and then use the output to AND with C.
- This is where we introduce the concept of signals.

---
Signal
- The VHDL code of this circuit is written here.
- The signal here is AB that works as an intermediate signal inside the blackbox.
- We have to declare the signal after architecture and before begin.